Illumina Team
Opentron Workflow

---
Input Sample QC- BR dsDNA
OPENTRONS
199ul/well
Master mix
6 cycles of Mixing
EMPTY PLATE (96 WELL)
BLACK NUNC PLATE
2mins Incubation in Dark
Clariostar
SAMPLE PLATE (from Biobank) (96 WELL)
HSP
1ul/well
Prepare EXCEL sheet
Reservoir
Thermofisher

---
PRE LIBRARY PREP NORMALIZATION
Volume based on EXCEL sheet
Thermo-
fisher
       RSB
Mixing
Semi-skirted
Total vol: 25uL
NORMALIZED PLATE (96WELL)
SAMPLE PLATE (from Biobank) (96 WELL)
Volume based on EXCEL sheet

---
 Library QC-HS ssDNA
199ul/well
Master mix
6 cycles of Mixing
2mins Incubation in Dark
Clariostar/ Qubit
LIBRARY PLATE (MANUAL/AUTOMATION (96 WELL)
1ul/well
Prepare EXCEL sheet

---
 LIBRARY NORMALIZATION
Volume based on EXCEL sheet
Themo-
fisher
       RSB
2.5 nM Concentration_EMPTY PLATE (96 WELL)
SEMI SKIRTED
TOTAL VOL: 25uL
Mixing
NORMALIZED PLATE (96WELL)
LIBRARY PLATE (MANUAL/AUTOMATION (96 WELL)
SEMI-SKIRTED
Volume based on EXCEL sheet

---
 LIBRARY POOLING &DILUTION
POOL 15 uL OF NORMALIZED LIBRARIES (2.5nM) INTO A SINGLE TUBE
S1-S24
S73-S96
S49-S72
S25-S48
310 uL OF POOLED LIBRARIES
Adding 78 uL of 400mM Tris_HCl
Adding 77 uL of 0.2N NaOH
(310 uL of 2.5nM Pool +1.9 uL of 2.5nM PhiX) + 77 uL of 0.2N NaOH
Manual
8 min. Incubation
Transfer to Library Tube
DILUTION TO 2.5nM PhiX
DILUTION TO 0.2N NaOH
7.5ul NFW +2.5ul PhiX
160 ul NFW + 40 ul NaOH
PhiX 10nM
PhiX 1N NaOH
2.5nM of PhiX
0.2N NaOH